## Slide 1: FOBAS
Periodical report
Notes: Right-click, select Format Background and change the Picture fill, File

## Slide 2: Contents
  FOBAS report status traffic light system 3
  Distribution of reports 4 - 5
  Global benchmarking and report distribution 6 - 11
  Port frequency 12
  Supplier frequency 13 - 14
  Sum of bunker quantity as per BDN 15 - 16
  Global red report distribution 17
Analysis Observations 18 - 23
  Reported Problems 24 - 30
  Overall Evaluation 31
  Contract utilization details 31

## Slide 3: FOBAS report status traffic lights
  Green – Normal
    Within specification - cleared for use
  Amber - Caution
    Within specification but analysis results indicate fuel has particular storage, treatment and/or handling requirements to ensure safe use
  Red – Action
  Off specification and/or high risk
    Important to read report on receipt
    “FOBAS Specialist will contact client by phone to discuss remedial options.”

## Slide 4: Distribution of reports

## Slide 5: Distribution of bunker samples

## Slide 6: Distribution of bunker samples per vessel

## Slide 7: Benchmarking Global vs <<client>>

## Slide 8: Distribution of amber reports per parameter
Notes:
Al & Si is considered elevated when the concentration exceeds 40 mg/kg.
Sometimes amber reports contain more than one off specification parameter. This could mean the number of red reports doesn’t match the number of red parameters.

## Slide 9: Distribution of red reports per parameter
Notes:
Al & Si is considered elevated when the concentration exceeds 40 mg/kg.
Sometimes red reports contain more than one off specification parameter. This could mean the number of red reports doesn’t match the number of red parameters.

## Slide 10: Distribution of amber results per supplier and parameter

## Slide 11: Distribution of red results per supplier and parameter

## Slide 12: Frequency of ports used

## Slide 13: Frequency of suppliers used

## Slide 14
Visualization of suppliers used
Lloyd's Register

## Slide 15: Sum of bunker quantity supplied as per BDN (HFO)

## Slide 16: Sum of bunker quantity supplied as per BDN (MGO)

## Slide 17: Time required from sampling date to lab receipt date

## Slide 18: Benchmarking total time from sampling date to lab receipt date

## Slide 19: Global red report distribution

## Slide 20: Analysis Observations
  Al & Si content
  Sulphur – Exhaust gas emissions
  Density observations
  Water content
  Total sediment potential analysis
  Ignition quality

## Slide 21: Al & Si Content - samples tested with Al & Si > 40 mg/kg.

## Slide 22: Al & Si Content - samples tested with Al & Si > 40 mg/kg visualised.

## Slide 23: Al & Si Analysis Distribution

## Slide 24: Al & Si Content - Recommendations
In cases where Al& Si content of the fuel is elevated, following guidelines may be considered:
Fuel to be kept in settling tanks for maximum possible time to allow for separation by gravity.
Settling tank should be drained off for water/sediments at regular intervals, observing any change in the degree of water/sediment being drained.
Operating purifiers in parallel/series as per machinery manufacturer’s guidelines.
De-Sludge cycle frequency may be increased to ensure that the bowl is kept clean and providing maximum design efficiency to separate the cat fines from the fuel oil.
Close monitoring of the fuel pump index on main engine and generating machinery fitted with plunger and barrel assembly type fuel pumps in respect to set power output whilst this fuel is in use.
Close monitoring of the cylinder liner and piston ring pack condition during the use of this fuel.

## Slide 25: Sulphur – Exhaust Gas Emissions
  ECA Compliance
No samples have been noted to fail compliance with MARPOL Annex VI Reg. 14.1.2 (max. S content outside ECA- SOx at 3.50% m/m). <<No.>> No samples have been noted to fail compliance with MARPOL Annex VI, Reg. 14.4.3 and the EU Directive requirement for EU ports (max S content at 0.10% m/m).
<<No.>> No samples have been noted to fail compliance with MARPOL Annex VI, Reg. 14.1.3 and the EU Directive requirement for EU ports (max S content at 0.50% m/m).
These comments offered with regard to the application of the Annex VI and the EU Directive are those of 'an informed observer' and it should be noted that any final ruling can only come from the respective Flag State, Port State Control or the appropriate department of the Administration of the Annex VI Signatory State within whose waters the ship(s) affected are to operate and which may itself be guided / directed by advice from the International Maritime Organisation (IMO).

## Slide 26: Sulphur – Exhaust Gas Emissions / Best Practices
If tested sulphur content exceeds the sulphur requirement
Supplier should be put on notice and requested to comment on the FOBAS finding regarding the sulphur content of the fuel.
Sample(s) of the subject fuel oil in storage tank(s) (assuming it has not been mixed upon loading) - from top / middle / bottom levels - should be tested to confirm the result of the initial bunker drip sample.
Subsequent to outcomes from points 1 and 2 above (as applicable), Flag State and relevant Bunker Supplier Registration Authority and Port State(s) should be duly advised and their guidance be requested.
Keep all records such as BDNs, log book entries, communications to relevant parties, fuel loading, transfer and change over details in good order.

## Slide 27: Density Observations
Importance of the fuel density is dual –
It has both technical and commercial implications
It needs to be ensured that the vessel's purification system can handle the density of the fuel.
As a rule of thumb, density differences of 0.010 kg/l should be monitored and discussed.
Tested density lower than the density stated on the bunker delivery note (BDN) indicates potential short-loading of the vessel.
Based on analysis results and BDN advised data for bunkerings during this period, two significant differences have been noted between advised and tested densities, as per below table.
On top of tested density value, the received volume and the representativeness of the sample should also be confirmed. Any contractual agreements made between the purchaser and supplier should be taken into consideration.

## Slide 28: Density differences > of 0.010 kg/l

## Slide 29: Water Content
    Water in fuel
    Water easily finds its way in the fuel and when up to certain levels, it requires neat maintenance in order to be removed. Water presence in the fuel increases the load of the purifiers, affects the fuel lubricated components of the fuel system and, if present in the combustion chamber, may lead to formation of highly corrosive acids. Density and viscosity will affect the performance of settling tanks and purifiers with respect to the water removal.
    From a commercial aspect, water contained in the fuel directly affects the true quantity of fuel loaded.

## Slide 30: TSP Analysis
Sediment
  ISO-8217-2012, maximum TSP content is set at 0.10% m/m. Total sediment measurement aims at indicating the tendency of the fuel to sludge deposition.
Sediment may be attributed to either external contamination (dirt, water) or to precipitation of the inherent asphaltenic components of the fuel.
In extreme cases, fuels with free asphaltenic components can ‘break up’ causing significant technical implications.
The ‘break up’ is dependent on the nature of the liquid hydrocarbons in which the asphaltenes are suspended. Once a fuel has chemically broken down there is no way to reverse the process.
If sediment is high, it should be monitored and discussed.
<<No.>> of total sediment failing the ISO specification have been noted among bunker samples from this period.

## Slide 31: CCAI / Ignition Quality
CCAI
Calculation of the Carbon Aromaticity Index (CCAI) is an empirical index based on the measured fuels density and viscosity. It gives a general indication of the ignition properties of the fuel.
Contemporary marine fuels are products of intensive blending, so they require specific attention with regards to their ignition and combustion quality.
During use with diesel generators and generally during low load operations, it is more likely for ignition and combustion quality implications to be experienced.
There are test methods (e.g. with use of FIA) to outline a fuel’s combustion and ignition profiles, which can be applied when more information is required.

## Slide 32: Overall evaluation

## Slide 33: Thank you
Remember, you have your own website portal at www.lrgmt.com. Using this will allow you to see pending samples, all your analysis reports, statistics based on your fleet, suppliers used etc., bulletins, technical documentation and more. If you don’t have access to your portal, please let us know by contacting us at fobas@lr.org, and we will arrange it for you.